## Slide 1: Using Super-Resolution on Face Recognition
Presenter: Sheng-Hsing Hsiao
Advisor: Jyh-Shing Roger Jang
Dept. of CSIE, National Taiwan University, Taiwan

## Slide 2: Outline
Introduction
Related Work
Approach
Experiments
Conclusion
References
Notes: 不要全部大寫

## Slide 3: Introduction
  Faces, a basic attribute that can distinguish one person to another. There are many well-known face recognition models have deployed on modern computer vision and multimedia applications.
  In real world, the face recognition models need to meet the actual cases to identify the low-resolution human faces. It is essential to explore how to achieve an efficient method without losing too much on recognition accuracy.
  To address this problem, we proposed a model reconstructing the high-resolution faces before recognition. In addition, we used FaceBoxes to detection faces and VGGFace with Resnet50 backbone as the face feature extractor can run 14 FPS on NVIDIA Quadro GV100 GPU.
Notes: 不要寫全部

## Slide 4: Related Work
Low-resolution Face Recognition in the Wild via Selective Knowledge Distillation
  Two-stream convolutional neural network
https://arxiv.org/pdf/1811.09998.pdf
Notes: 老師stream是來分辨高解析度的圖
學生stream是分辨相對應低解析度的圖
老師stream會輸出最有用的face features 藉由解決sparse graph optimization
再用這些feature來fine tune學生stream 不佳s

## Slide 5: Related Work
FSRNet: End-to-End Learning Face Super-Resolution with Facial Priors Two-stream convolutional neural network
https://arxiv.org/pdf/1711.10703.pdf
Notes: 粗的SR 網絡來生成粗的HR 圖像。然後，粗的HR圖像會被送到兩個分支
細的SR encoder 來feature extractor
另外就是Prior Estimation Network估計landmark heatmap 和解析圖
接著將這兩個結果輸入到一個細的SR decoder
然後為什麼不直接從LR來抽feature 或是預估landmark 因為ＬＲ上比較模糊複雜度比較高
landmark 則提供面部關鍵點的準確位置
面部解析估計不同面部組件的分割
先驗信息對人臉超分辨率的影響
把先驗信息估計網絡移除以後，構建了一個Baseline網絡
用了先驗信息的模型有提高，分別提高了0.4dB（加入landmark heatmap），1.0dB（加入解析圖），1.05dB（兩個都加）
解析圖比landmark heatmap含有更多人臉圖像超分辨的信息，帶來的提升更大。
全局的解析圖比局部的解析圖更有用
landmark數量增加所帶來的提升很小。
FSRGAN的兩項指標（PSNR/SSIM）都不如FSRNet，但是從視覺效果上看更加真實。這也與目前的一個共識相對應：基於生成對抗網絡的模型可以恢復視覺上合理的圖像，但是在一些指標上（PSNR , SSIM）的值會低。而基於MSE的深度模型會生成平滑的圖像，但是有高的PSNR/SSIIM。

## Slide 6: Related Work
FSRNet / FSRGAN
https://arxiv.org/pdf/1711.10703.pdf
Notes: 粗的SR 網絡來生成粗的HR 圖像。然後，粗的HR圖像會被送到兩個分支
細的SR encoder 來feature extractor
另外就是Prior Estimation Network估計landmark heatmap 和解析圖
接著將這兩個結果輸入到一個細的SR decoder
然後為什麼不直接從LR來抽feature 或是預估landmark 因為ＬＲ上比較模糊複雜度比較高
landmark 則提供面部關鍵點的準確位置
面部解析估計不同面部組件的分割
先驗信息對人臉超分辨率的影響
把先驗信息估計網絡移除以後，構建了一個Baseline網絡
用了先驗信息的模型有提高，分別提高了0.4dB（加入landmark heatmap），1.0dB（加入解析圖），1.05dB（兩個都加）
解析圖比landmark heatmap含有更多人臉圖像超分辨的信息，帶來的提升更大。
全局的解析圖比局部的解析圖更有用
landmark數量增加所帶來的提升很小。
FSRGAN的兩項指標（PSNR/SSIM）都不如FSRNet，但是從視覺效果上看更加真實。這也與目前的一個共識相對應：基於生成對抗網絡的模型可以恢復視覺上合理的圖像，但是在一些指標上（PSNR , SSIM）的值會低。而基於MSE的深度模型會生成平滑的圖像，但是有高的PSNR/SSIIM。

## Slide 7: Approach
Input Image
… Amy Kevin Tom …
intruder
Face Detection
Yes
Face Verification
Below the
threshold
Pass the
threshold
No
Face Alignment
System flowchart
Notes: 話flowchart

## Slide 8: Approach
Kevin
Face verification flowchart
Input Image
Face Feature Extractor
Compare the distance of existing vectors
Below the threshold
Select the nearest
Pass the
threshold
intruder
Notes: 話flowchart

## Slide 9: Experiments
Experimental Settings
  OS: Ubuntu 16.04
  CPU: Intel(R) Xeon(R) CPU E5-2630 v4 @ 2.20GHz
  GPU: GeForce GTX 1080 Ti
  Memory: 128GB
  Code language: Python 3.6.7

## Slide 10: Experiments
Face Detection
  Faceboxes: A CPU real-time face detector with high accuracy
https://arxiv.org/pdf/1708.05234
Notes: Rapidly Digested Convolutional Layers 主要是解決速度問題
快速的縮小feature map的大小
採用C.ReLU activation function
使用CRelU來保證輸出維度不變的情況下，減少卷積核數量
Multiple Scale Convolutional Layers(MSCL)
類似於SSD，在網絡的不同層進行檢測
作者提出來的點就在於增加小的anchor的訓練
定義了anchor 密度 來平衡對密度不足的anchor來增加偏移訓練

## Slide 11: Experiments
MTCNN: Joint Face Detection and Alignment using Multi-task Cascaded Convolutional Networks
https://arxiv.org/abs/1604.02878
Notes: 在2016年提出的一個multi-task 論文的人臉偵測還有人臉特徵同時進行
給定一張照片的時候，將其縮放到不同尺度形成圖像金字塔，以達到尺度不變
總共有三個CNN cascade
3個stage對人臉的處理是按照一種由粗到細的方式
pnet是一個全卷積網絡(FCN)，全卷積網絡的優點在於可以輸入任意尺寸的圖像，生成人臉分類、一些bounding box、還有人臉上的landmark
使用Bounding box regression的方法來校正這些候選窗
使用非極大值抑制（NMS）合併重疊的候選框

## Slide 12: Experiments
Evaluate the Face Detection Performance
  Datasets
    Pascal Face
      450 frontal face images of 27 or so unique people.
      Some examples:
    AFW
      205 images with 473 labeled faces
      Some examples
Notes: 要有混淆矩陣

## Slide 13: Experiments
Evaluate the Face Detection Performance
  Intersection over Union (IOU)
    An Intersection over Union score > 0.5 is normally considered a “good” prediction. Depending on the metric, threshold usually be set to 50%, 75% or 95%.
    True Positive (TP): A correct detection. Detection with IOU ≥ threshold
    False Positive (FP): A wrong detection. Detection with IOU < threshold
    False Negative (FN): A ground truth not detected
    True Negative (TN): Does not apply.

## Slide 14: Experiments
Evaluate the Face Detection Performance
  Precision Recall curve
Notes: An object detector of a particular class is considered good if its precision stays high as recall increases, which means that if you vary the confidence threshold, the precision and recall will still be high.

## Slide 15: Experiments

## Slide 16: Experiments
Super-Resolution
  WDSR (Wide Activation for Efficient and Accurate Image Super-Resolution, CVPR Workshop 2018)

## Slide 17: Experiments
Super-Resolution Dataset: VGGFace2 (A large scale image dataset for face recognition)
  9,000 + identities
  3.3 million + faces
  362 ~ per-subject samples
My method
  Select images whose shape above 1k as our training data.
  Face alignment according bounding boxes provided by the dataset.
  Downscale these images x1/2, x1/3, x1/4.

## Slide 18: Experiments
Downscale the high-resolution images

## Slide 19: Experiments
HR
Bicubic X4
WDSR X4
HR
Result of the WDSR on VGGFace2

## Slide 20: Experiments
Face Recognition Dataset: LFW Face Dataset
  5749 celebrities, each contains 1~10 images, 13233 images in total
My method:
  For each celebrity, downloaded 10 images from google.
  Applied Vgg16/Resnet50/Facenet face feature extractor to encode these images and merged to a NumPy array.
  Encoded every image in LFW dataset and calculated the distance with each person’s feature.

## Slide 21: Experiments
Evaluate Face Recognition on LFW (1x)
Chart: Accuracy
| Top-1 | Top-3 | Top-5
VGGFace (Resnet50 ) | 0.8094 | 0.8578 | 0.8691
VGGFace (VGG16) | 0.5133 | 0.611 | 0.6479
Facenet | 0.7187 | 0.7951 | 0.8169
Notes: 抽feature講清楚for face

## Slide 22: Experiments
Results of Bicubic and Super-resolution
HR
Bicubic4x
SR4x
Divided4x

## Slide 23: Experiments
Results of Bicubic and Super-Resolution on LFW
Chart: Top-1 Accuracy
| 2X | 4X
Bicubic | 0.7669 | 0.3851
SR | 0.7701 | 0.3244
DividedSR | 0.7358 | 0.2839

## Slide 24: Experiments
Inside-test Dataset
  CASIA-FaceV5 (as our authorized users)
    2,500 color facial images of 500 subject, each has 5 images
    For each user, 4 images for the user vector, 1 image for the inside-test
    All face images are 16 bit color BMP files and the image resolution is 640*480
http://biometrics.idealtest.org/dbDetailForUser.do?id=9
Notes: http://biometrics.idealtest.org/dbDetailForUser.do?id=9 改標題

## Slide 25: Experiments
Outside-test Dataset
  Helen dataset (as our intruders)
    2000 images as the outside test set
    If there are multiple faces in the picture, select the one closest the image center as the test face.

## Slide 26: Experiments
Face Verification Confusion Matrix
  Ground Truth
  = 1 for authorized user, 0 for intruder
  Face Verification System
  False Accept means system will incorrectly accept an access attempt by an unauthorized user.
  False Reject means failing to recognize an authorized person and rejects that person as an intruder.
Confusion Matrix |  |  | 
 |  | 1 | 0
 | 1 | True Accept | False Reject
 | 0 | False Accept | True Reject
Confusion Matrix |  |  | 
 |  | 1 | 0
 | 1 | True Accept | False Reject
 | 0 | False Accept | True Reject
Notes: http://www.mecs-press.org/ijigsp/ijigsp-v6-n2/IJIGSP-V6-N2-6.pdf

## Slide 27: Experiments
Face Verification ROC curve

## Slide 28: Experiments
Penalty Matrix
  Ground Truth
  Face Recognition System
  Care about False Positive; the lower, the better
Confusion Matrix |  |  | 
 |  | +1 | -1
 | +1 | 0 | 1
 | -1 | 100 | 0
Confusion Matrix |  |  | 
 |  | +1 | -1
 | +1 | 0 | 1
 | -1 | 100 | 0

## Slide 29: Experiments
Face Verification ROC curve
Notes: x threshold y penlty

## Slide 30: Experiments
Accuracy of different feature extractor
  Select the threshold by the lowest Equal Error Rate (ERR)
 | Resnet50 | VGG16
ERR | 4.77% | 16.72%
Accuracy | 99.8% | 94.2%
Notes: EER是（一個分類器的）ROC曲線（接受者操作特性曲線）中錯分正負樣本概率相等的點（所對應的錯分概率值 數值比率寫出來
增加錯誤分析與acc敘述

## Slide 31: CONCLUSION

## Slide 32
Thank you for your attention